## Slide 1: A Scalable and Privacy-Aware IoT Service for Live Video Analytics
Junjue Wang, Brandon Amos, Anupam Das, Padmanabhan Pillai*, Norman Sadeh, Mahadev Satyanarayanan
Carnegie Mellon University and Intel Labs*

## Slide 2: Video Cameras are Ubiquitous Today
David Barrett. 2013. “One surveillance camera for every 11 people in Britain, says CCTV survey.” Daily Telegraph (July 10, 2013).
Notes: 1. Video cameras are ubiquitous:
Surveillance camera  widely used
Lightweight portable camera  popular among adventurers and travelers
Head-mounted wearables with cameras  begin to see
2. A survey in the U.K.: one surveillance camera for every 11 people in a public space

## Slide 3: Live Video as a Service offers high value
3rd Party Analytics
Liquid Spill!
Lost Child!
Icy Patches!
Checkout line too long!
Unattractive Window Display
Notes: Transition: With the ubiquity of cameras, live video as a service high value
two unique strength of cameras as sensing devices:
Open-end  third-party
Examples

## Slide 4: Bandwidth and Privacy Concerns
Analytics
Cloudlet
Privacy Concerns
Limited Bandwidth
Analytics
Cloud
Analytics
Cloud
scalable
Extracted Output of Analytics
Extracted Output of Analytics
Privacy-Aware:
(Real-time, Full Resolution)
Notes: Transition: However, to achieve such reality, there are 2 major hurdles
Hurdles:
Bandwidth Consumption: stress b/w in aggregate network in cloud-computing paradigm
User’s privacy concerns: rich that sensitive data (owner of the device, but also bystander)
This project, prototype system solves this problem:
New computing paradigm, edge computing
Real-time blurring/denaturing at full-frame rate to remove sensitive data, at the correct time and volume
We focus on a particular use case of face denaturing as a proof of concept
Design Goals: scalable, real-time, full resolution of the video stream

## Slide 5: Privacy Mediator Architecture
Edge Computing
Small, multi-tenant data centers (cloudlets) close to IoT devices
Separation of Trust
Improved Scalability
Video
Deco-ding
Privacy Mediator VM
Cloudlet
Analytics VMs

Analytics
Algorithm 1
Analytics
Algorithm 2
Analytics
Algorithm 3
Extracted
information
sent to
cloud
Denaturing Policy
Input
Video
Stream
Archived
Denatured Video
Encrypted originals of obscured bits
Denaturing
Algorithm
3rd Party Installable
Notes: Transition: To solve the bandwidth problem, we used the privacy mediator proposed by Nigel.
Describe Privacy Mediator:
Instead of streaming videos to the cloud, videos are streamed to a computational devices nearby, referred as cloudlet. (could be in cellular tower, could be a power machine sitting in your home)
Privacy mediator VM (water treatment plants)
  Video decoding
  Denaturing
  Store encrypted sensitive data
Denatured video streams publish to analytics running on the cloudlet.
2 benefits
Separation of Trust: can be a trusted software module. Platform integrity of a mediator is ensured by running on a cloudlet (trusted domain of the data owner)
Improved Scalability: (stress)
compare to cloud: distilled information (water treatment plants, we don’t build them at a centralized location. Build them near where the water source)
compare to mobile devices: much more computation power and not restricted battery life
Previous paper, talks about the concept. We want to make the concept concreate. We Provide the underlying service in blue

## Slide 6: Denaturing, the trade-off between privacy and value
Denaturing: the process of making video “safe” from a privacy viewpoint
Examples of Denatured Video Frames
High Accuracy
Real-time
Full Resolution
Notes: Transition: edge computing solves the b/w problem. We also tackled the privacy problem as well
The concept of Denaturing:
Definition
Trade-off between privacy and value
Different denaturing mechanism also enables different levels of protection:
Face detection  simpler
Face Recognition: mall example. A mother to track his/her own children
We focus on using face recognition to achieve real-time performance

## Slide 7: Video: Remove Unknown Faces

## Slide 8: Video: Remove Faces by Identity

## Slide 9: OpenFace - Accurate Face Recognition
Inspired by FaceNet (CVPR 2015)
Trained with 500K images from public dataset (CASIA-WebFace + FaceScrub)
DNN + SVM Approach
  DNN to extract facial features
  SVM to classify faces
Notes: Transition: Privacy concerns, we need a highly accurate face recognition module
Problems:
state-of-art commercial system are trained with proprietary product data, for example from social networks
Trained with millions of data
Inspired by FaceNet, we built our own DNN model and trained it with public available data
DNN based model
Pipeline: image, face detection, extract facial features into 128 feature vectors. Every face turned into a vector. Classification using SVM
Benefit of combined approach:
1. Only need to train neural networks once and offline
2. Adding new identities into the system is fast, since SVM training is fast (on the orders of milli-seconds)

## Slide 10: OpenFace - Accuracy on LFW benchmark
Predict whether pairs of images are of the same person
Chart: 
| 0 | 0.5 | 1
random | 0 | 0.5 | 1
False Positive Rate
True Positive Rate
Notes: Close to state-of-art commercial recognition, close to human accuracy. Evaluated on a standard computer vision benchmark
ROC:
Definition
Random guess
Ideal ROC Curve
AUC
More in our paper:
Show short training time
Recognition speed
Classification up to 100 people identity

## Slide 11: Detection and Recognition are Slow
30ms per face
127ms per
1280x720 frame
Processing speed in a VM running on a 4-core Intel® Core™ i7-4790 processor @3.6 GHz with Hyper-Threading, and no GPU.
Face
Detection
Face Recognition
(OpenFace)
Input
Video
Stream
Bounding
Boxes
of Faces
Bounding
Boxes
With Identities
< 7 FPS
with only 1 face
Notes: Transition: A highly accurate face recognizer is not enough. We need to steady throughput to be at real-time, full frame rate
Timing breakdown:
Detection
Recognition
Given h/w, we want to be able to support as many camera streams as possible

## Slide 12: RTFace - Tracking-based Denaturing Pipeline
Input
Video
Stream
Dispatcher
Tracker
1 Tracked Face Initially
Face
Detection
Face Recognition
(OpenFace)
Frame Revisit Buffer
Denature Region of Interests
Denaturing Policy
Encrypted originals of obscured bits
To
Analytics
VMs
Revalidation
Bounding
Boxes
of Faces
(10, 15,
88, 95)
(20, 28,
87, 92)
Bounding
Boxes
With Identities
“Jason”
“Jerry”
Notes: Transition: Driven by throughput speed and scalability, we built a tracking-based pipeline
Walk-through the common scenario
Assume: there is a face already detected
Dispatcher: determines whether to use cheap tracking or expensive detection and recognition
Tracker: put into a queue
FRB: store the image temporarily. (Similar to a water reservoir)
Detection & recognition: update tracker asynchronuously
Example: another face detected
Images in the FRB will be revalidated by the tracker
In the end, denatured region of interests

## Slide 13: Evaluation - Scale with Number of Cameras
Multi-stream Frame Rate on 4-core Cloudlet with HD videos
Notes: Transition: With the tracking-based pipeline, we’re able to achieve an order of magnitude improvements over baseline
Baseline: we down-sample as people usually do. With original videos, our wins will be larger
We can also support more streams given a fixed h/w

## Slide 14: Summary
Privacy Mediator Architecture
OpenFace
RTFace
Optimizations to Reduce Privacy Leaks
Controlled Reversal of Denaturing
IoT Service Deployment at Enterprise Scale
Design Choices for Cloudlets
Notes: Transitions: Highlights of our solution, other materials I didn’t cover

## Slide 15: Q & A
Full Video Demo
https://goo.gl/gbtCLd

## Slide 16: Back Up

## Slide 17: RTFace – Optimizations to Reduce Privacy Leaks
Dispatch Criteria: Confidence score + Fail-safe mode
Detection Bias
Rapid Update Tracking
Frame Revisit Buffer
Notes: Remove, refer to paper

## Slide 18: RTFace - Tracking is accurate and effective
YouTube Celebrities Face Tracking and Recognition Dataset (320x240)
Dlib face detector’s output as “ground truth”
Overall, RTFace achieves 89 FPS, 92% accuracy while the naive pipeline achieves 12 FPS
Notes: Resolution 320x240
Naive solution 9 fps

## Slide 19: Controlled Reversal of Denaturing
Public safety or other societally important considerations override privacy considerations
Notes: Terrorist attack
the crucial clues in identifying the perpetrators of the 2013 Boston
Marathon terrorist attack were obtained from surveillance cameras.
Mediator doesn’t retain old keys
Most rencently denatured video is at risk of exposure
Remove, refer to paper

## Slide 20: IoT Deployment Architecture at Enterprise Scale
Notes: Alert people about these cameras (reasons for opt-in) enterprise
  Decentralized arch for camera network
Reduce # of candidate pool ( another channel using beacons), reduce # of working set
1 slide on additional work in paper:
Controlled reversal
Multiple cameras networks, decentralized
Scoping face population for a given camera
Scalability considerations

## Slide 21: Evaluation - Design Choice for 1 Gbps LAN
Notes: Netflix recommends 25 Mbps bandwidth for streaming 4K videos
5 Mbps

## Slide 22: OpenFace Accuracy on LFW Classification

## Slide 23: OpenFace Training Time on LFW Classification
8-core Intel Xeon E5-1630 v3 @ 3.70GHz CPU with OpenBLAS

## Slide 24: OpenFace Prediction Time on LFW Classification
8-core Intel Xeon E5-1630 v3 @ 3.70GHz CPU with OpenBLAS and a NVIDIA Tesla K40 GPU

## Slide 25: Previous Work on Image Privacy and De-identification
Previous Work on Content-Based Image Privacy
Offline / Sample of the Input Data
Not Real-time
Human assisted
Previous Work on De-identification
Assume the locations of sensitive areas are known
Focus on effective image modifications to preserve the anonymity
Complimentary to our work
Notes: Move to the end

## Slide 26: Evaluation - Scale with Quality of Cameras

## Slide 27: OpenFace - Accuracy on LFW benchmark
Predict whether pairs of images are of the same person
Close to commercial state-of-art classification accuracy
Short training time (ms) to add a new face
Recognition takes tens of ms
Notes: Close to state-of-art commercial recognition, close to human accuracy. Evaluated on a standard computer vision benchmark
ROC:
Definition
Random guess
Ideal ROC Curve
AUC
More in our paper:
Show short training time
Recognition speed
Classification up to 100 people identity

## Slide 28: Speeds of Critical Operations

## Slide 29
By July 2015, 6.7 hours of video were being uploaded to YouTube each second. The cumulative upload bandwidth of these videos is equivalent to only 24,120 cameras simultaneously streaming HD videos. This is two orders of magnitude smaller than the estimated 5.9 million security cameras in UK in 2013. Netflix recommends 25 Mbps bandwidth for streaming 4K videos. At that data rate, 100 buildings with 100 cameras each will need a 250 Gbps aggregation network to a metro-wide cloudlet.